# Current shunt amplifier circuits
There are many situations where the current in a circuit needs to be measured. Techniques to achieve this generally fall into 3 categories:
a) a small value series resistor, usually called a current shunt;
b) a Hall effect device that amplifies the magnetic field generated by the current;
c) a sensing MOSFET that separates a small fraction of the current and puts that through a (larger value) current shunt.
Which solution is appropriate depends on many factors including the level of current, the accuracy required and the response time or frequency of measurement.
Using a current shunt may be the simplest but does require an amplifier to bring the value into the measurement range of the analog to digital converter (ADC).
A current shunt may be placed in the high side or low side of a circuit. Consider a solar panel and a battery as shown in the diagram below.

The resistance of the shunt (or other device in series with the current) is a consideration, with competing issues of power dissipation in the shunt, and the voltage developed across it.
Table of devices, resistance, power loss and voltage (to be added).
### High side current shunt and amplifier
Here is a simple high side current shunt and amplifier circuit.
The current shunt is a 10 milli-ohm (0.01 ohm) resistor. The amplifier consists of two PNP transistors, Q1 and Q2. The collector resistor series on Q1 has been selected to give a 2.5 volt output above ground at zero current.
The behaviour of this circuit, as simulated by ngspice, is shown in the charts below.
In this chart the blue line shows the voltage at Vout as the current is changed from -5 amps to +5 amps. It is a smooth curve starting at about 0.6 volts when the current is -5 amps, passes through 2.5 volts when the current is 0 amps, and reaches 4.8 or 4.9 volts when the current is 3.5 amps.
The red line shows a calculated reference using the equation (Va-Vk)*50+2.5 which would be an ideal result for this amplifier.
The curve in the blue line would mean that a non-linear equation would need to be used to derive the actual current from the measured voltage. An equation that is within 0.1 volts of the blue line is
2*exp((va-vk)*20)+(va-vk)*15+0.5. Better equations may exist.
This chart shows the tracking of this equation (red line) with the simulated performance (blue line).

The next question is, how can I control the gain of this amplifier to allow for greater currents, and possibly improve the linearity?
Try putting resistors between the shunt connections and the emitters of Q1 and Q2.